## Slide 1: IoT ESP32 MCU workshop 101
SPD IoT 101 workshop (5 Sept 2019)
Internet of Things 101 Workshop (14 Sept 2019)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/iot-esp32-mcu-workshop

## Slide 2: SDK installation
https://github.com/yeokm1/iot-esp32-mcu-workshop
Install Serial Virtual Com Port drivers for your operating system if needed
  https://www.silabs.com/products/development-tools/software/usb-to-uart-bridge-vcp-drivers
Install Arduino IDE:
  https://www.arduino.cc/en/main/software
Install ESP32 SDK addon to Arduino IDE
  Add the following path to Additional Boards URL configuration
  https://dl.espressif.com/dl/package_esp32_index.json

## Slide 3: Components Check
ESP32 breakout board
50cm micro-USB cable
Half-size breadboard
Bunch of wires
In ESD bag
  Red LED
  Push button
  330 ohm resistor
  10k ohm resistor
330 ohm resistor
10k ohm resistor

## Slide 4: Agenda
Background of ESP32 and Arduino
Basics of electronics
  Serial - Setting up of software SDK and testing
  Blink - Connecting and blinking LED
  Button - Connecting button and try to detect press
  Debounce - Concept of input debouncing
The “Internet” portion of IoT
  Post - Posting Request to a server on button press
  Get - Repeatedly polling the server for on or off instruction

## Slide 5: Who made the ESP32?
Made by Espressif Systems based in Shanghai
Fabless semiconductor company
Founded by Singaporean Teo Swee Ann in 2008

## Slide 6: ESP32 chip vs ESP32 module vs ESP32 breakout

## Slide 7: ESP32 Specs
Specs | Value
CPU | Xtensa dual/single-core 32-bit LX6 microprocessor, operating at 160/240 MHz
RAM | 520 KiB
Flash memory | 4 - 16 MiB
Network Connectivity | Wifi 802.11n 2.4Ghz + BT 4.2
Peripheral Interfaces | 3x UART, 2x SPI, 2x I2C, ADC, SD touch sensors, etc

## Slide 9: Why not single-board computers like Raspberry Pi?
Specs | Arduino-compatible ESP32 | Raspberry Pi 4 B
CPU type | Microcontroller | Microprocessor
Speed | Dual Core 160/240Mhz | Quad core 1.5 Ghz
RAM | 520KB | 1 - 4 GB
GPU/Display | None | VideoCore VI GPU, 4K
Disk | 4 MiB | Depends on microSD card
Other connectivity | Wifi 802.11n 2.4Ghz + BT 4.2 | USB, Ethernet, HDMI, audio, Wifi 2.4/5Ghz 802.11ac, BT 5.0
Operating System | None | Linux (usually Raspbian)
Real Time Operation | Better | Poorer
Typical Power consumption | 0.8W | 8W
Price (SGD) | $30 | $50 - $80

## Slide 10: Arduino SDK
Easy to use cross-platform IDE for microcontroller programming
Support for many microcontrollers
C/C++ language
Numerous libraries

## Slide 11: 01-Serial
Verify Arduino SDK installed correctly as in the parent README.md
How to flash an Arduino program?
Using the serial console and ESP32 log facility

## Slide 12
Magnifying glass opens serial console
Show Timestamps
Newline
115200 baud

## Slide 13: 02-Blinky
Connect an LED
Blink from the LED

## Slide 14: Half/Full Breadboard
Base Prototyping component
Continuous lines indicate those holes are connected together
Horizontal usually for power
Convention: Red for +, Black/Blue for -
Vertical for your components

## Slide 15: LED
“A light-emitting diode (LED) is a semiconductor light source that emits light when current flows through it. ”
Diode: Component allowing one-way current flow
Anode +: Longer leg
Cathode -: Shorter Leg

## Slide 16: Resistor
Resists the flow of current
Resistor Colour bands
4-band 330 ohm
  Orange, Orange, Brown, Gold
  3, 3, x10, 5% tolerance
4-band 10K ohm
  1, 0, x1000, 5% tolerance
  Blown, Black, Orange, Gold

## Slide 17: Connecting the LED setup
Unplug USB cable before working on electronics
Breadboard + ESP32 board (G32, GND) + 330 ohm resistor + LED + wires
Pinouts may differ slightly from diagram. Always check the pin labels!
GND
G32

## Slide 18: Program the board with 02-blinky.ino

## Slide 19: 03-button button setup
10k ohm resistor + button + wires -> G34
Actual breakout 3V3 pin position differs from picture
“Pull down” resistor setup
GND
3V3
G32
G34

## Slide 20: Pull down resistor for button
Resistor “pulls” IO32 to ground when button is released
Guarantees that IO35 pin goes to 0
GND
3V3
G32
G34

## Slide 21: Program the board with 03-button.ino
We want to toggle LED on each button press
Observe looping speed of button press detection is too fast to be useful

## Slide 22: 04-debounce
Process one input within an interval

## Slide 23: 05-wifi-post
Making a POST request to the server via a button press
Able to receive a POST request using a Go program
WIFI_SSID: iot-workshop
WIFI_PASS: esp32isgreat
HOST: …

## Slide 24: 06-wifi-get
Making a Get Request to a server to get instruction
Serve a GET request using a Go program
WIFI_SSID: iot-workshop
WIFI_PASS: esp32isgreat
HOST: …

## Slide 25: Why LED needs a resistor?
The ballast resistor is used to limit the current through the LED and to prevent damage
Minimum Resistor calculation for LED only
  LED Specification: 1.8V drop, max 20mA current
  ESP32 pin source voltage: 3.3V
  Minimum Resistance for LED
But ESP32 has a pin current limit of 12mA
  Minimum Resistance to satisfy ESP32 limits
In testing: 12mA current supplied to LED is too bright
  So we use a higher resistance like 330 ohm to further drop the current